        NEW FW TO ADD DAYLIGHT SAVINGS 21-10-2020

Down load the zip folder called (FW96675A bin G2KSR1 FW 20201020V01)
Unzip the folder and copy and paste the FW96675A.bin file to a formatted SD card, insert the SD card into dash cam and turned the device ON
A red flashing led will blink until the device switches back ON the firmware is now updated.
Please format the SD card once completed you can format the SD card from the device, or remove the SD card from the device while the device is ON and format it on a computer. PLEASE DO NOT TURN THE DASH CAM OFF AFTER THE UPDATED FIRMWARE IS COMPLETED, PLEASE REMOVE THE SD CARD FIRST.
The new firmware added the daylight savings and time zone, Please adjust according to where you live.