ADDING UHD 24 P RESOLUTION IN THE DASH CAM MENU

SOFTWARE VERSION AT-2019.08.08

This version is only if you are using a cigarette charger this is not for hard wire kit.

Format SD card, copy FWG200A.bin file to the card.

Remove card insert the card in the dash cam, make sure the dash cam remains off.

Turn the dash cam on, the dash cam will automatic read the Firmware

from the card, a white led will flash on and off, once the flashing stops

the dash cam will boot up ready for recording.

Go to the menu in settings and scroll to format card, this must be done or the unit will update the firmware again when the unit switches on.

The new update shows the UHD P24 in the resolution in the dash cam menu.