        UPDATE FIRMWARE FOR VERSION 20200021_V0.7

The new FW will add reverse guide lines on both cameras when the reverse trigger is active.
NOTE
There is no setting in the menu to turn this option off, So please make sure you understand before
you update the FW.

PROCEDURE
Copy the SD_CarDV.bin file onto a formatted SD card.
Insert the card into the GRV92MTK mirror make sure the unit is off before inserting the card.
Turn ON the unit, the firmware will automatically start loading the firmware, DO NOT interrupted
the power while updating.
When firmware has completed please format the card again to remove the bin file.