- put “host.h16”into usb device,

- unit play usb

- hold to press disp+1 key , unit is in sw updating

- unit automatically power off when it finish sw updating.

- pull out built-in ISO connector（OR COMPLETELY CUT OFF THE POWER SUPPLY） ,then connect it with unit again

- Power on CEM2101 again,

- At radio mode, press disp+4 to look at sw version as  V 033

- SW upgrade successfully