14D-12 sensor painting instruction

We supply two sensor colors: black and silver.

If you need to paint dark color, use black sensor. If you need paid light color, use silver sensors.

1. Key down the original paint (use scotch pad).

2. When spray paint, remove the out ring and paint the out ring and sensor separately.

3. In 1 hour later, use your thumb to remove the paint off the silicon ring.

4. When dry thoroughly, put them back.

Please kindly download the video from link below:

http://1drv.ms/1hv2T8i